## Slide 1: Medial axis computation of exact curves and surfaces
M. Ramanathan
Department of Engineering Design,
IIT Madras
http://ed.iitm.ac.in/~raman

## Slide 2: Various skeletons
Curve skeletons
Mid-surface
Chordal axis transform (CAT)
Straight skeleton

## Slide 3: Definition
Medial Axis (MA) locus of points which lie at the centers of all closed balls (or disks in 2-D) which are maximal.
MAT = MA + Radius function

## Slide 4: Input / Output
Exact representation – Curve/surface equations
Discrete representation – Point-set, voxels, tessellated, polylines, bi-arcs
  Output
Continuous-Approximate
Continuous-Exact
Discrete-Approximate
Discrete-Exact

## Slide 5: Approaches
Wavefront propagation
Divide and conquer
Delaunay triangulation / Voronoi
Numerical tracing
Thinning
Distance transform
Bisector-based

## Slide 6: Approach and input
Divide and conquer – Polygons, Polyhedra
Wavefront – Polygons (Curvilinear)
Delaunay/Voronoi – Point-set
Thinning and distance transform - Images

## Slide 7: For exact representation
Bisectors in closed form - point, lines, conic curves.
Rational only for point-freeform curve, between two rational space curves.
In general, bisector between two rational curves is non-rational.
Bisectors, even between two simple geometries, need not be simple.

## Slide 8: Bisector examples

## Slide 9: Bisectors vs. MA

## Slide 10
Divide and conquer looks to be too complex
In a similar way, wavefront propagation also looks tedious.
Either numerical tracing of MA segments or symbolic representation of bisectors.

## Slide 11: Tracing Algorithm

## Slide 12: Tracing Algorithm (Contd.)

## Slide 13: Curvature constraint

## Slide 14: 2D, 2.5D and 3D Objects

## Slide 15: Definition (Voronoi cell)
Consider C0(t), C1(r1), ... , Cn(rn), disjoint rational planar closed regular C1 free-form curves.
The Voronoi cell of a curve
C0(t) is the set of all points
in R2 closer to C0(t) than to Cj(rj), for all j > 0.
C1(r1)
C2(r2)
C3(r3)
C4(r4)
C0(t)

## Slide 16: Definition (Voronoi cell (Contd.))
We seek to extract the boundary of the Voronoi cell.
The boundary of the voronoi cell consists of points that are equidistant and minimal from two different curves.
C0(t)
C1(r1)
C2(r2)
C3(r3)
C4(r4)
C0(t), C3(r3)
C0(t), C4(r4)

## Slide 17: Definition (Voronoi cell (Contd.))
The above definition excludes non-minimal-distance bisector points.
This definition excludes self-Voronoi edges.
r1
t
C0(t)
C1(r)
r3
r4
r
“The Voronoi cell consists of points that are equidistant and minimal from two different curves.”
p
q
r2
t

## Slide 18: Definition (Voronoi Diagram)
The
Voronoi Diagram (VD) is the union of the
Voronoi Cells (VC) of all the free-form curves.
C0(t)

## Slide 19: Outline of the algorithm
tr-space
Lower envelope algorithm
Implicit bisector function
Euclidean space
C0(t)
C1(r)
Limiting constraints
Splitting into monotone pieces

## Slide 20: Key Issues
C0(t)
C1(r1)
C0(t)
C1(r1)
C0(t)
C1(r1)
C2(r2)
Can the branch or junction points be identified without computing the bisectors or even portion of bisectors?

## Slide 21: Our methodology
Voronoi neighborhood between two curves is created/changed at minimum distance point/branch point.
Hence these special points are solved for directly.
Minimum distance as antipodal or two touch disc.
Branch disc (BD) as three touch disc (TTD)

## Slide 22
Initially all pairs of minimum antipodal discs (MADs) are solved and store in a list.
MADs are processed in increasing order of radius in the list.
Whenever discs are added connectivity information is maintained.
Three touch discs (TTDs) is solved for only when relevant neighborhood is formed and inserted into the list .
All consistent antipodal lines
Minimum radius antipodal

## Slide 23: Illustration of the basic idea
Initial Radius list
After processing Rab, Rbc
TTD of (Ca, Cb, Cc) added
TTD is processed to decide if it is a branch disc

## Slide 24: Emptiness check of ADs

## Slide 25: Algorithm steps

## Slide 26: Algorithm continued
1
4
2
3
5

## Slide 27: Results

## Slide 28: Salient features
Given a curve of degree m, the degree of the bisector is 4m − 2. Computing TTD or AD has a degree of m+(m−1).
Instead of step sizes or intersection of bisectors, a simple directed edge existence is used.

## Slide 29: VD for non-convex curves and medial axis

## Slide 30: Approach vs. Input

## Slide 31: Comparison for different inputs

## Slide 32: What’s next
Use bisector-less approach for 3D freeform surfaces to compute Junction points
Focus will be on reducing computational complexity.
Speeding up of computation using utilities such as GPU.
Relation between the elements in the MA to that of the object.

## Slide 33: References
Ramanathan M., and B. Gurumoorthy " Constructing Medial Axis Transform of Planar domains with curved boundaries,", Computer-Aided Design, Volume 35, June 2003, pp 619-632.
Ramanathan M. and B. Gurumoorthy " Constructing Medial Axis Transform of extruded/revoloved 3D objects with free-form boundaries ", Computer-Aided Design, Volume 37, Number 13, November 2005, pp 1370-1387
Ramanathan M., and Gurumoorthy B., "Interior medial axis computation of 3D objects bound by free-form surfaces" , Computer-Aided Design, 42(12), 2010, 1217-1231
Iddo Hanniel, Ramanathan Muthuganapathy, Gershon Elber and Myugn-Soo Kim "Precise Voronoi Cell Extraction of Free-form Rational Planar Closed Curves ", Solid and Physical Modeling (SPM), 2005, MIT, USA, pp 51-59
Bharath Ram Sundar and Ramanathan Muthuganapathy, " Computation of Voronoi diagram of planar freeform closed curves using touching discs " , Proceedings of CAD/Graphics 2013, Hong Kong.

## Slide 34: Discussions Q & A