## Slide 1: RCM within the AMS
RCM and Reliability Centered Maintenance – there’s a difference
The relationship of AMS to Reliability Centered Maintenance
What exactly is “failure data”?
Failure data timeline (“how best to capture this data”)
Life of a Defect – “that pesky critter”
Asset Offender report – the world’s best Pareto
Webinar
22 may 2015
John Reeve
Practice Leader
Maintenance & Reliability

## Slide 2
O&M Vision
Goal Statement

## Slide 3: What is purpose of Asset Management
The main objective is to make more informed decisions regarding facilities & assets as to recurring problems, repair/replace criteria, failure trending and work force efficiency.
We want to
reduce unplanned breakdown maintenance, and also
optimize the use of your labor resources.
But this requires an accurate database and a
well established process - - an ideal process.
By enhancing asset reliability
Improving work force productivity
because
Reactive maintenance has a higher cost
Reduce reactive maintenance and optimize use of labor resources
+
Predict and prevent as opposed to
fail and fix.
Notes: The primary goal of maintenance is to avoid or mitigate the consequences of failure of equipment. This may be by preventing the failure before it actually occurs which PM and condition based maintenance help to achieve. It is designed to preserve and restore equipment reliability by replacing worn components before they actually fail. Preventive maintenance activities include partial or complete overhauls at specified periods, oil changes, lubrication and so on. In addition, workers can record equipment deterioration so they know to replace or repair worn parts before they cause system failure. The ideal preventive maintenance program would prevent all equipment failure before it occurs.
The challenge is to have the right resource to capture the right information and use it to make the right decision.
Computerized data collection, storage, and reporting capabilities allow facilities to cover more equipment, more frequently with fewer workers.

## Slide 4
Defining … RCM Analysis
RCM Analysis … is a structured framework for analyzing the functions and potential failure modes for a physical asset in order to develop a maintenance task that will provide an (a) acceptable level of operability, (b) with an acceptable level of risk, (c) in an efficient and cost-effective manner.
What are the functions and associated desired performance standards of the asset in its present operating context (functions)?
In what ways can it fail to fulfil its functions (functional failures)?
What causes each functional failure (failure modes)?
What happens when each failure occurs (failure effects)?
In what way does each failure matter (failure consequences)?
What should be done to predict or prevent each failure (proactive tasks and tasks intervals)?
And, what should be done if a suitable proactive task cannot be found (default actions)?
Identify PM/PdM

## Slide 5
ATM
Machine
PIN
Authenti-
cation
Dispense
Cash
Process Step
Potential Failure Mode
Potential Failure Effect
SEVERITY
OCCURRENCE
RPN
Recommended Action
Potential Causes
Risk Priority Number is to be applied to the Failure Mode
(RPN) to help identify priority actions
DETECTABILITY
Function Failures Effects Consequences Process Maintenance
Controls Task
Notes: Severity is impact of failure event.
Occurrence is frequency of occurrence (of the failure event).
Detection is the ability of process control to detect.
The RPN is the total multiplication.

## Slide 6
CC
CCH
Activated Carbon
Combustion Gas Cleaning & Exhaust
Blower
(1)
Transport air at pressure
Silo
(2)
Provide bulk storage of power activated carbon
Piping
(3)
Convey PAC to ductwork
F1
Motor bearing failure
M1
PDM: Vibration analysis
Freq
FreqUnit
Store FMEA and Strategy in AMS screen
Notes: FMEA
………………………………………………………………………………………………………………
What: Failure mode and effect analysis (FMEA) is the study of potential failures that might occur in any part of a system to determine the probable effect of each failure. The purpose is to prevent failures using a simple and cost-effective analysis that draws on the collective information of the team to find problems and resolve them before they occur.
Why: The analysis is known as a bottom-up approach to finding each potential mode of failure and preventing failures that might occur for every component of a system. FMEA can be performed from different viewpoints such as safety, mission success, availability, repair costs, failure modes, reliability reputation, production processes, follow-on service, and so forth.
When: FMEA is most productive when performed during the design process to eliminate potential failures. It can also be performed on existing systems where O&M staff are made team members to add real-life experiences to educate the team in a problem-solving forum that is constructive to eliminating existing problems.
Where: The analysis can be conducted in the design room or on the shop floor and it is an excellent tool for sharing experiences.
……………………………………………………………………………………………………….
Evaluation Criteria for Reliability-Centered Maintenance (RCM) Processes states that: Any RCM process shall ensure that all of the following seven questions are answered satisfactorily and are answered in the following sequence:
What are the functions?
The main function should clearly identify what the equipment is intended for and all of the performance standards it is expected to maintain including environmental, health and safety standards. Below is an example main function statement for a chilled water system and its corresponding Functional Failures:
Chilled Water System Main/Primary Function Statement:
To be able to supply high quality, chilled water at a temperature of 40°F plus or minus 5°F and a rate of 120 gallons per minute while meeting all environmental, health, and safety standards.
Functional Failures of the Chilled Water System
Unable to supply chilled water at all
Unable to maintain water temperature above 35° F
Unable to maintain water temperature below 45° F
Unable to supply water at a rate of 120 gallons per minute
Unable to maintain water quality standards
Unable to maintain (company, state or government) environmental, health or safety standards
2. What are the functions and associated desired standards of performance of the asset in its present operating context (functions)? > In what ways can it fail to fulfill its functions (functional failures)? > What causes each functional failure (failure modes)? > What happens when each failure occurs (failure effects)? > In what way does each failure matter (failure consequences)? > What should be done to predict or prevent each failure (proactive tasks and task intervals)? > What should be done if a suitable proactive task cannot be found (default actions)?
Failure effect: Finally, we briefly describe the consequence of the failure mode should it occur. To be complete, this is usually done at three levels of assembly—local, system, and plant. In describing the effect in this fashion, we clearly see the buildup of the consequences. With our jammed gate valve, the local effect at the valve is "stops all flow." At the system level, "no fluid passes on to the next step in the process," and finally, at the plant level, "product production ceases (downtime) until the valve can be restored to operation."
Thus, without a clear understanding of failure terminology, reliability analyses not only become confusing, but also can lead to decisions that are incorrect
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
An FMEA completed on DC machines in an Australian Steel mill revealed the following most likely causes of DC machine failure to be:
Contamination of motor by Dust, Dirt fumes etc. (where was the PM?)
Inadequate maintenance practices. (Internal and contract)
Inadequate brush tension (technician)
Over tensioning of belts or shaft misalignment. (technician)
Overheating due to ineffective ventilation (plant engineer)
Neutral axis and compounding issues.
Overloading. (operator)
Inadequate lubrication, i.e. too much or not enough. (technician)
Incorrect or ineffective protection devices. (plant engineer)
Note: it is important to identify the “defect”.
These findings were used to improve the existing PM’s with excellent results. Over a 3 year period there was a 70% reduction in DC motors that failed in service.

## Slide 7: How do you achieve operational excellence?
Maintenance & Reliability Program
basic
failure
analysis
advance scheduling techniques
defect
elimination
condition
monitoring (PdM)
You create a
Reliability Centered Maintenance
involving
RCM analysis
Answer:
maintenance task
definition
The product of Maintenance is Reliability
*
*
Notes: The product of maintenance is reliability
A reliable asset is an asset that functions at the level of performance that satisfies the needs of the user.

## Slide 8
Terminology
SW
Core Team
Business Rules
Analytical Reports
Long Range Plan
Defect Elimination
Reliability is defined as the probability that a device will perform its required function under stated conditions for a specific period of time.
Maintainability … the relative ease, time/labor with which an item can be diagnosed, retained, and restored.
Notes: The relative ease and economy of time and resources with which an item can be retained in, or restored to, a specified condition

## Slide 9
Reliability Centered Maintenance
AMS Standards
Benchmarking
5-year AMS plan
Business rules
Change tracking
Work Mgmt
Work planning
Backlog mgmt
Advance scheduling
Outage mgmt
PM/PdM program
WO Feedback
ODR/TPM
Kaizen/brainstorming
FMEA
RCA; Defect elimination
Action Tracking
Database accuracy
Failure data
Actual costs
Job status
End-game: analytical rpts
Repetitive Failure History
KPIs & metrics
Incident Tracking
Blended training
Maintenance playbook
Back-
Log
Mgmt
Planning
PM /
PdM
program
Business
Rules
AMS Change Request
Tracking
End-Game
w. Analytical Reports
FMEA
Repetitive
Failure
History
Database
Accuracy
AMS
Long Range
Plan
KPIs
and
Metrics
Bench-
marking
Actual
Costs
Maint.
Playbook
Blended
Training
Action
Tracking
Job Complete
updates
ODR (TPM)
WO Feedback
Scheduling
Otg
Mgmt
Root Cause Analy.
Defect Elimination
Failure
Data
Kaizen
Asset
Management
System
Reliability Centered Maintenance

## Slide 10
But Challenges Remain
Software Procedure Responsibilities
Process and Roles and
Bill Broussard, Emerson Process Management, 07/29/2008

## Slide 11: More “bad data” quotes
[Tracy Strawn] Since no one trusts the data, reports are not generated. This begins the slippery slope of marginalizing the AMS; therefore, because no one uses it, the system must not be important.
[MRG survey] only 20% felt their AMS fully supports effective asset management due to faulty data.

## Slide 12
The key word is “may”
Reliability Leaders
There are two camps:
Condition Monitoring, RCM, FMEA, RCA, defect elimination advocates
and
Asset Management System
solution providers
PdM Practitioners
As seeing is believing …
… they don’t believe.
The PdM Practitioners are doubtful
Mobius Institute slide

## Slide 13
70% of all installations do not perform any basic failure analysis.
90% do not capture adequate failure data
90% do not capture asset condition
WO Feedback is not formally captured
Somewhere at the site there is a senior manager asking “Where’s the ROI?” [ which usually refers to reports]
(based on JR field observations)
The Facts are this and they are undisputed

## Slide 14: The Result of capturing failure data is better decision making through failure analysis
The RCM Analysis identifies FAILURE MODEs
The AMS should be able to capture the FAILURE MODE on the work order.
Then compare results

## Slide 15
It all starts with the Failure Data
WO #
ASSET #
TYPE FAILURE
PROBLEM CODE
WORKTYPE
PROBLEM DESCRIPTION
WO PRIORITY
FAILED COMPONENT
STATUS
ACTION VERB
CAUSE
WO FEEDBACK
ACTUAL COSTS
Labor
Material
Services
Work Order Initiation
Completion
TOTAL DOWNTIME
Some of these fields may not be on your AMS screen, and
The ability to capture failure data depends on working level participation
(which is needed for the failure analytic)

## Slide 16
It all starts with the Failure Data
WO #
ASSET #
TYPE FAILURE
PROBLEM CODE
WORKTYPE
PROBLEM DESCRIPTION
WO PRIORITY
Work Order Initiation
Describe the Problem – not the remedy
Select the lowest level asset
Select Worktype which indicates REPAIR
FULL
PARTIAL
POTENTIAL
DEFECT
EMERGENCY
URGENT
ROUTINE
ROUTINE – HIGH
ROUTINE – MOD
ROUTINE - LOW
OPERATIONS
MAINTENANCE
FAILED COMPONENT
STATUS
ACTION VERB
CAUSE
WO FEEDBACK
ACTUAL COSTS
Labor
Material
Services
Completion
TOTAL DOWNTIME
Note: I would capture Asset Condition under monthly PM
Repair Event

## Slide 17
It all starts with the Failure Data
WO #
ASSET #
TYPE FAILURE
PROBLEM CODE
WORKTYPE
PROBLEM DESCRIPTION
WO PRIORITY
Work Order Initiation
This is the component-part that failed
ADJUST, ASSEMBLE, CLEAN, INSPECT, MACHINE, MODIFY, REBUILD, REPLACE-EQ, REPLACE-PART, LUBRICATE, TRAIN
FAILED COMPONENT
STATUS
ACTION VERB
CAUSE
WO FEEDBACK
ACTUAL COSTS
Labor
Material
Services
Completion
TOTAL DOWNTIME
This is the physical cause.
Examples include:
ERROR-OPER
ERROR-MAINT
PM FREQUENCY
PM/PdM WRONG
PM/PdM MISSING
PWR FAILURE/SURGE
IMPROPER MATERIAL
MISSING PARTS
MISSING DOCS
NORMAL WEAR
Note: There are other CAUSE levels. The system designers could decide to add more cause fields.
COMPONENT PROBLEM
Problem code associated with Component

## Slide 18
The Failed Component is part of the Failure
Mode
Centrifugal Pump
the components are
is the asset

## Slide 19
A problem code is the first observation by an O&M Technician of a problem regarding the asset.
Problem Codes ( an example list )

## Slide 20
COMPONENT | PROBLEM CODE
TUBE FRAME | COLLAPSED
SOLAR CELL | FRACTURED
THERMISTOR | OPEN/CLOSED
HYDROGEN STORAGE | HIGH TEMPERATURE
PIPING | LEAKAGE
CHECK VALVE | STUCK
SHEET ROLLER | JAMMED
SWITCH | NO-OPEN
BATTERY | NO POWER
MOTOR | NO OPERATE
Failure == Component-Part + Component-Problem
Mode

## Slide 21
4 Levels of Cause Codes
Physical
Human
Systemic
Latent
“failure analysis” to component
“root cause failure analysis”
Notes: Note: lubrication (too much, too little, wrong type, contamination) is the number one cause of bearing failures.

## Slide 22
Aging
An aging asset can last 25-50 years.
4%
-----------
PM / PdM
A
Under basic wear & tear asset can last 1 mo. - 7 yrs.
Basic
12%
-----------
PM / PdM
B
Careless
Induced flaws can limit asset life from 1 day - 1 year
84%
-----------
some
EM / UR
C
C01
Raw Materials
21%
C02
Operating the asset
29%
C03
Workmanship
21%
C04
C05
8%
Incorrect-inferior part
21%
Design
Level-2 Cause
xx
HUMAN
HUMAN
HUMAN
HUMAN
HUMAN

## Slide 23
Asset
Problem Code
Type Failure
Cause Code
OPERATOR
GATEKEEPER (reviews new WO; may adjust priority)
PLANNER/SCHEDULER (plans/schedules the work)
MAINTENANCE TECHNICIAN
MAINTENANCE SUPERVISOR (responsible for accuracy)
RELIABILITY ENGINEER
Update AMS
Update AMS
Update AMS
FAILURE DATA
WO INITIATION
GATEKEEPER
PLANNER/
SCHEDULER
TECH
STARTS JOB
TECH
UPDATES
REL ENGR
UPDATES
3-D Failure Data Model
Component-Problem
Component-Part
Asset Downtime
WO Feedback
JOB DONE
Actual Costs

## Slide 24
Goal: find & remove the Defect

## Slide 25
World’s Best Pareto
Notes: Don’t let imperfect data hold you back, but rather strive to understand and work with the data’s limitations. Blend data analysis with interviews. There is no substitute for face-to-face discussion with the people who operate and maintain the equipment. This communication serves two purposes: it validates or invalidates the results and it shows people that the data is being used. Used data breeds better data. Do not allow yourself to completely discount the value of the data. Doing nothing because the data is perceived as being inaccurate does not advance anything. As with condition monitoring, act on the findings and then broadcast the value. Achieving good equipment reliability is a journey without end.

## Slide 26
Create SQL to drill-down on the Failure Mode

## Slide 27
What have we Learned?
The Failure Mode is not generally understood or captured on work orders in most AMS products. | Potential Failure Modes should be identified using RCM Analysis. Short of that, they should be captured on WO failure history – and stored in the AMS. The failure mode should be a concatenation of Component-Part and Component-Problem.
Failure Data in general is not being captured. | This is due to a variety of reasons: The AMS entry screens may need tailoring ; Choice lists need to be created; Rules for entry must be clarified; The timeline for entry needs to be understood; and different roles enter different data pieces. Lastly, the maint. staff needs to be trained on importance.
Failure Analytics do not generally exist. | The AMS stakeholders are responsible for designing this report (pen on paper). This can then be built – and implemented. With the report in-hand you may discover that additional failure data fields need to be added to screen & captured.
Database inaccuracy is sometimes a “reason” for NOT running analytics. | Failure data may be missing or inaccurate but this should never be a reason for not running a Failure Analytic (e.g. Asset Offender report).
Database inaccuracy is still an issue however | The “core team” should do everything possible to improve accuracy by getting the right fields on screen; establishing good value lists; conducting training; addressing change mgmt issues; and process audits - - i.e. leave nothing to chance
The Problem

## Slide 28
S
T
A
T
U
S
PROCESS
INTERACTION
You Need a Roadmap
because it helps to know where you are going

## Slide 29
The Setup will be Critical
Roadmap
Failure Data
Asset
Management
System Design

## Slide 30
Knowledge
Base
Asset Offender report
Failure History
Business Rules
WO initiation must-enter failure data
WO completion must-enter failure data
Route WO to Reliability Team for asset review where appropriate
Operator
Planner/Scheduler
Maint. Supervisor Reliability Engineer
Reliability Team
Verify WO updates correct
Review WO feedback
The objective is to improve
asset
reliability
Failure Data fields

## Slide 31
You, [insert your name], can make a difference
Thanks for
listening
All companies have the potential to improve asset reliability and with minimal configuration you can support Reliability Centered Maintenance
Failure Data
Failure Analytics
Manage by Exception
Get the Right Data Build the Right Report Make Better Decisions
Contact Information:
Presenter – JReeve@CohesiveSolutions.com
Exec. VP CIS – Mlogsdon@CohesiveSolutions.com
Consulting Services Mgr - SMccarthy@cohesivesolutions.com
Notes: The Cohesive CMMS system 5-year Plan represents a combination of stakeholder requirements and industry best practices which when combined provide a complete roadmap for operational excellence. We leverage our years (decades) of client site experiences plus tips and tricks for asset performance & reliability management. There are several deliverables included in this project scope – the most important being the resource-leveled long range plan (schedule) for CMMS optimization & utilization identifying optimized process/procedure and supporting roles. For example, you may have used Maximo for over 10 years but never established a reliability tCMMS. Or, there is no understanding of basic failure analysis or backlog management. Key data elements may never have been captured which are critical for management & analytical reporting. Or worse yet, the current data is mostly ‘cactus’.
As an organization, if you do not have a 5-year plan the odds are great that you are reacting to short-term requirements. Although day-to-day continuous improvement is a good thing, the long range plan asks the entire organization “why not, how can we get there, and when”. Sometimes the leadership tCMMS needs to be challenged as to vision, direction and approach. The Cohesive consultant directs & leads a project tCMMS in discussion using a variety of workshops to establish where we are, where we want to end up, and what are the current problems (data, process, culture). One of these workshops involves visioning. In this venue we ask for thoughts & ideas from stakeholders and visionaries. We ask the audience to think of future perfect – and visualize what this would look like. It may be seemingly impossible at present to get there but if you never set the goal …you certainly never will.