## Slide 1
NetWave 2nd Generation Product Overview
  Guy Walker
  North America Trainer A&E Program Manager

## Slide 2
wireless

## Slide 3: Primary Applications
Remote Location
Point-to-Point
NVR

## Slide 4: Primary Applications
Multiple Locations
Point-to-Multipoint
NVR

## Slide 5: Primary Applications
Creating “Line of Sight”
Daisy Chain / Drop & Repeat
NVR

## Slide 6: Primary Applications
Self Healing Ring
Using IEEE Spanning Tree Protocol
NVR

## Slide 7: Primary Applications
Backhaul
High Bandwidth

## Slide 8
NVR
NW7
NW8
NW9
NW7
NW1/M
NW1
NW8
NW9
Hybrid Topologies
NW7/M
Notes: ComNet also makes a complete line of Ethernet extenders using the VDSL2 technology.
It’s different because it is an asymetrical transmission technology originally designed for poor copper cabling over longer distances.
This is a very valuable product when you need to get any kind of bandwidth out to much longer distances.
You can see these can get out to 10,000 feet.
i.e. Think of an electrical sub-station that’s 8,000 feet from any type of network drop. It’s only 1Mbps, but that’s better than putting in a microwave relay…

## Slide 9: Wireless Ethernet Products
Power, Point & Play
  Pre-configured AP and Client
  Mount and connect AP to AC or PoE source and the network.
  Mount and connect Client to AC or PoE source and camera.
  Point them at each other until you get green signal strength LEDs.
  Done.
NWK7

## Slide 10
NWK1
Point-to-Point Preconfigured Kit
Includes MAC-locked AP and Client
New IP67 ABS enclosure – glands and LEDs on bottom
Fully hardened -40˚ to 75˚C
Dual 10/100 Ethernet ports
Powered by PoE or included PIM
5GHz 802.11a/n radio
95 Mbps Max. throughput
Up to 2 miles distance
19dBi Internal antenna with 17° Beam
Includes power injection modules (PIM1)
Includes mounting brackets for 2 ½” pole
NetWave Generation 2

## Slide 11
NW1
Point-to-Multipoint
Up to 15 clients
New IP67 ABS enclosure – glands and LEDs on bottom
Fully hardened -40˚ to 75˚C
Dual 10/100 Ethernet ports
Powered by PoE or included PIM
5GHz 802.11a/n radio
95 Mbps Max. throughput
Up to 2 miles distance
19dBi Internal antenna with 17° Beam
Includes power injection module (PIM1)
Includes mounting bracket for 2 ½” pole
NetWave Generation 2

## Slide 12
NW1/M
Point-to-Point
Smaller enclosure
New IP67 ABS enclosure – glands and LEDs on bottom
Fully hardened -40˚ to 75˚C
Single 10/100 Ethernet ports
Powered by PoE or included PIM
5GHz 802.11a/n radio
95 Mbps Max. throughput
Up to 2 miles distance
16dBi Internal antenna with 30° Beam
Includes power injection module (PIM1)
NetWave Generation 2

## Slide 13
NW7 & NWK7 High Throughput
Point-to-Point
Point-to-Multipoint
Up to 15 clients
New IP67 ABS enclosure – glands and LEDs on bottom
Fully hardened -40˚ to 70˚C
Dual Gigabit Ethernet ports
Port 1 is a PD, port 2 is a PSE
Powered by PoE or PIM
5GHz 802.11a/n radio
120 Mbps full duplex throughput
180 Mbps Max. throughput in one direction
Up to 4 miles distance
19dBi Internal antenna with 17° Beam
Optional antennas for AP
NetWave Generation 2

## Slide 14
NW7/M High Throughput
Point-to-Point
Smaller enclosure
New IP67 ABS enclosure – glands and LEDs on bottom
Fully hardened -40˚ to 70˚C
Single Gigabit Ethernet port
Powered by PoE or included PIM
5GHz 802.11a/n radio
120 Mbps full duplex throughput
180 Mbps Max. throughput in one direction
Up to 4 miles distance
16dBi Internal antenna with 30° Beam
Includes Gigabit power injection module (PIM2)
NetWave Generation 2

## Slide 15
NW8 High Throughput Dual Radio
Daisy Chain
Self-Healing Ring
IP67 enclosure
Fully hardened -40˚ to 75˚C
Dual Gigabit Ethernet ports
Port 1 is a PD, port 2 is a PSE
Powered by PoE or PIM
5GHz 802.11a/n radio
120 Mbps full duplex throughput
180 Mbps Max. throughput in one direction
Up to 2 miles distance
19dBi Internal antenna with 17° Beam
External antennas for radio 2
NetWave Generation 2

## Slide 16
NW9 Ultra High Throughput
Point-to-Point
802.11ac rated radios
Casted aluminum enclosure – glands/LEDs on bottom
Fully hardened -40˚ to 70˚C
Dual Gigabit Ethernet ports
Port 1 is a PD, port 2 is a PSE
Powered by PoE or PIM
867 Mbps radio throughput
500 Mbps Max. throughput in one direction
Up to 4 miles distance
19dBi Internal antenna with 17° Beam
NetWave Generation 2

## Slide 17
NetWave Generation 2
Model | Enclosure | Ethernet Ports | PD | PSE on Port 2 | Internal Antenna | External Antenna Compatible | PIM included | Max Speed (true thrpt) | NWBKT Compatible
NW1 | ABS | 2 x 100Mbps | Yes | No port 2 | 17˚ | No | Yes/FE | 95Mbps | Yes
NW1/M | ABS Mini | 1 x 100Mbps | Yes | No | 30˚ | No | Yes/FE | 95Mbps | No
NW7 | ABS | 2 x 1000Mbps | Yes | Yes | 17˚ | No | No | 180Mbps | Yes
NW7/M | ABS Mini | 1 x 1000Mbps | Yes | No port 2 | 30˚ | No | Yes/GIG | 180Mbps | No
NW8 | Original NetWave | 2 x 1000Mbps | Yes | Yes | 17˚ | Yes | No | 180Mbps | Yes
NW9 | Casted | 2 x 1000Mbps | Yes | Yes | 17˚ | No | No | 500Mbps | No

## Slide 18
NetWave Solar
  Everything but the pole:
  120Watt PV solar panels
  Lead Acid Gel Batteries
  Power controller, injector
  NEMA enclosure
  All cables & mounting brackets
4 Kits Based On:
  15W or 30W continuous output
  3 or 6 hours of peak sunlight
  40 hours reserve battery
NetWave Solar

## Slide 19
NetWave Battery Backup
  277 VAC at the pole, but only at night:
  Valve regulated lead acid batteries
  Smart DC-UPS power controller
  Power inverter or injector
  NEMA box
  Mounting brackets/straps
NetWave Battery Backup