Suggested Specifications For Model FB33

Adjustable Lift-Out Flood Barrier

# Part 1 - General

1.01	Description

Work Included: Provide flood barrier(s) factory assembled with frame(s) and hardware in accordance with the contract documents.

1.02       Standards

Comply with the provisions of (as applicable).

1.   AWS Structural Welding Code.

- ASME Structural Welding Code Section IX.

1.03       Submittals

Manufacturers Data: Submit installation and maintenance instructions for flood barriers.

Shop Drawings: Submit shop drawings for flood barriers including dimensioned plans and elevations, sections, connections and anchorage, and parts list.

Calculations (Optional): Submit calculations, approved by a qualified engineer, to verify the barrier’s ability to withstand the design pressure loading.

1.04       Qualifications

Experience: The manufacturer of the flood barrier(s) shall present evidence attesting to at least 5 years of successful experience in the design and manufacture of both the flood barrier and flood barrier seal of the type specified.

# Part 2 - Products

2.01	Flood barrier shall be Model FB33 as manufactured by Presray Corporation.

2.02	Materials

Panel: Carbon steel mechanical tubing.

Wall mount Frame:  ASTM A569 Carbon steel (stainless steel optional).

Finish: Panel—high solids mastic epoxy painted.  Wall frame: high solids mastic epoxy painted.

Seal: Chloroprene solid rubber sheet with closed cell foam outer gasketing.

Hardware:

Mounting anchors: Stainless steel when applicable.

Optional:

Multi-Panel Systems with removable mullions between panels for openings too wide to be accommodated by single panel.

2.03	Design

Flood barrier(s) shall provide an effective seal against the design flood level.

# Part 3 — Execution

3.01	Installation

Install flood barriers in accordance with manufacturer’s instructions and approved shop drawings.

# Part 4 — Warranty

- 4.01	1-year limited against defects and workmanship from date of shipment.

# Text boxes

Presray Corporation

Critical Containment

P.O. Box 200

Wassaic, NY 12592

Phone: (845) 373-9300

Fax: (845) 855 – 8034

www.presray.com

Email: technicalsupport@presray.com