Display hidden notes to specifier by using ‘Tools’/‘Options’/‘View’/‘Hidden Text’. On newer versions of Microsoft Word click on round Windows logo in top left corner, Click on ‘Word Options’ button at bottom of drop down menu. Click on ‘Display’ on left menu bar, and check the box for ‘Hidden Text’.

GENERAL

SECTION INCLUDES

Overhead coiling fire doors with integral frames.

RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

Section 05500 - Metal Fabrications: Support framing and framed opening.

Section 06200 - Finish Carpentry: Wood jamb and head trim.

Section 08710 - Door Hardware: Product Requirements for cylinder core and keys.

Section 09900 - Painting: Field applied finish.

Section 16130 - Raceway and Boxes: Conduit from electric circuit to door operator and from door operator to control station.

Section 16150 - Wiring Connections: Power to disconnect.

REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

ASTM A 653 - Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

ASTM A 666 - Standard Specification for Austenitic Stainless Steel Sheet, Strip, Plate, and Flat Bar.

ASTM A 924 - Standard Specification for General Requirements for Steel Sheet, Metallic-Coated by the Hot-Dip Process.

NEMA 250 - Enclosures for Electrical Equipment (1000 Volts Maximum).

NEMA MG 1 - Motors and Generators.

NFPA-80 – Standard for Fire Doors and Fire Windows.

DESIGN / PERFORMANCE REQUIREMENTS

Fire Rated Assemblies: Provide assemblies complying with NFPA 80 and listed in UL Directory or Intertek Testing Services (Warnock Hersey Listed) Directory.

SUBMITTALS

Submit under provisions of Section 01300.

Product Data:  Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Details of construction and fabrication.

Installation methods.

Shop Drawings: Include detailed plans and elevations, details of framing members, anchoring methods, clearances, hardware, and accessories.

** NOTE TO SPECIFIER **  Delete selection samples if colors have already been selected.

Selection Samples:  For each finish product specified, two complete sets of color chips representing manufacturer's full range of available colors and patterns.

Verification Samples:  For each finish product specified, two samples, minimum size 6 inches (150 mm) long, representing actual product, color, and patterns.

Manufacturer's Certificates: Certify products meet or exceed specified requirements.

Operation and Maintenance Data: Submit lubrication requirements and frequency, and periodic adjustments required.

QUALITY ASSURANCE

Manufacturer Qualifications: Company specializing in performing Work of this section with a minimum of five years experience.

Installer Qualifications: Installer Qualifications: Company approved by manufacturer, specializing in performing Work of this section with minimum three years experience, with IDEA Certified Installers and service technicians on staff.

DELIVERY, STORAGE, AND HANDLING

Store products in manufacturer's unopened packaging until ready for installation.

Protect materials from exposure to moisture. Do not deliver until after wet work is complete and dry.

Store materials in a dry, warm, ventilated weathertight location.

PROJECT CONDITIONS

Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results.  Do not install products under environmental conditions outside manufacturer's absolute limits.

COORDINATION

Coordinate Work with other operations and installation of adjacent materials to avoid damage to installed materials.

PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: Overhead Door Corp., 2501 S. State Hwy. 121, Suite 200, Lewisville, TX  75067.   ASD. Tel. Toll Free: (800) 275-3290. Phone: (469) 549-7100. Fax:	 (972) 906-1499. Web Site: www.overheaddoor.com. E-mail: info@overheaddoor.com.

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions:  Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

OVERHEAD COILING COUNTER FIRE DOORS WITH INTEGRAL FRAMES

Overhead Coiling Counter Fire Doors with Integral Frames: Model 662 Integral Frame Fire-Rated Counter Doors.

Label: Rolling fire doors shall bear the UL 1-1/2 Hour Class B label for masonry or non-masonry fire walls.

Curtain: Interlocking 22 gauge galvanized steel, flat profile slats with endlocks for curtain alignment and single angle bottom bar.

Integral Frame and Guides: 16 gauge stainless steel.

Hood: Stainless steel.

Finish:

** NOTE TO SPECIFIER **  Select the following paragraphs for the slat and hood materials required and delete the ones not required.

Galvanized Steel: Slats galvanized steel to ASTM A 653 finished with a rust-inhibitive roll coating process, including bonderizing, a 0.2 mils thick baked prime paint, and a 0.6 mils thick baked top coat.

Polyester coat finish in color as selected by Architect from manufacturer’s standard Gray or Tan colors.

Stainless Steel: Hood and frame stainless steel with No. 4 satin finish.

Non-galvanized exposed ferrous surfaces shall receive one coat of rust-inhibitive primer.

Sill: 14 gauge stainless steel sill enclosed with fireproof acoustic filler.

Bottom Bar: 10 gauge stainless steel with slide bolts and lift handles.

Brackets: Steel 11 gauge, primed.

Counterbalance: Helical torsion spring type. Counterbalance housed in a steel tube or pipe barrel, supporting the curtain with deflection limited to 0.03 inches per foot of span. Counterbalance is adjustable by means of an adjusting tension wheel.

Operation: Manual push up operation.

Locking: Interior slide bolts.

Mounting: Between jambs.

EXECUTION

EXAMINATION

Verify opening sizes, tolerances and conditions are acceptable.

Examine conditions of substrates, supports, and other conditions under which this work is to be performed.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Install in accordance with manufacturer's instructions.

Install rolling counter fire doors in compliance with requirements of NFPA 80. Test fire-release system and reset components after testing.

Use anchorage devices to securely fasten assembly to wall construction and building framing without distortion or stress.

Securely and rigidly brace components suspended from structure. Secure guides to structural members only.

Fit and align assembly including hardware; level and plumb, to provide smooth operation.

** NOTE TO SPECIFIER **  Select the following paragraph for electric operation of counter doors and delete if not required.

Coordinate installation of electrical service with Section 16150. Complete wiring from disconnect to unit components.

Coordinate installation of sealants and backing materials at frame perimeter as specified in Section 07900.

Install perimeter trim and closures.

ADJUSTING

Test for proper operation and adjust as necessary to provide proper operation without binding or distortion.

Adjust hardware and operating assemblies for smooth and noiseless operation.

CLEANING

Clean curtain and components using non-abrasive materials and methods recommended by manufacturer.

Remove labels and visible markings.

Touch-up, repair or replace damaged products before Substantial Completion.

PROTECTION

Protect installed products until completion of project.

END OF SECTION