## Slide 1
VisSim EMBEDDED
Encoder Basics
Use VisSim EMBEDDED to read a US Digital S4T quadrature encoder connected to a Texas Instrument F28069M LaunchPad

## Slide 2: Encoder
The F28069M LaunchPad board has two incremental quadrature encoder peripherals that manage the encoder count value and reset the count value each time an “index pulse” occurs.
The F28069M LaunchPad encoder connections are shown below:
The square pin (leftmost), labeled EP1A, is the Channel A signal. Moving rightward, the second pin, labeled EP1B, is the channel b signal, the third pin, labeled EP1I, is the index signal, the fourth pin is the 5 volt power signal, and the fifth pin is the ground signal.
Encoder 2 Connection
Encoder 1 Connection (pin 1 is leftmost rectangular pin)

## Slide 3: Encoder
Quadrature encoders measure rotational angle and direction by counting discrete “pulses”.
QEPA
QEPB
Time
As a quadrature encoder rotates, two square wave signals are generated, QEPA and QEPB.
CPR = # square wave Cycles Per Revolution of the encoder.
4 transitions per Cycle
PPR = Pulses Per Revolution = 4 * CPR
1 Cycle
Our encoder is a 256 CPR, so PPR = 4*256 = 1024

## Slide 4: Types of Encoders
Quadrature encoders measure rotational angle and direction by counting discrete “ticks”. Typically, an encoder will have between 256 to 4000 ticks per revolution.
There are two types of encoders:
Incremental: Although this type of encoder begins counting “ticks” at power up, it’s information is not accurate until an “index pulse” occurs. The “index pulse” occurs 1x/revolution. At power up, an incremental encoder must initially be rotated until the “index pulse” occurs before its angle data can be used.
Absolute: This type of encoder begins counting “ticks” at power up and provides accurate angle data immediately.
Encoders have 5 electrical connections: +5v, ground, A, B, index pulse
The A and B outputs consist of discrete values, 1 or 0, and are out of phase by 90 degrees, hence they are called quadrature. this allows the direction of rotation to be determined:

## Slide 5: Index Pulse
A VisSim model to detect the “index pulse” is presented below, In this model, the “index pulse” is named “EncoderIndexHasOccured”
When bit 2 of QEPSTS = 1, the “EncoderIndexHasOccured” discrete is set to 1 and remains there.
QEPSTS is the quadrature encoder status register

## Slide 6: Encoder – Test Model
The following model is used on an 8 pole PMSM. It detects the “Index pulse” and measures the electrical and mechanical angles. “Time Step” = .0001 sec.
“AngleElectricalNormalized” = normalized (0-1 = 0-360 degrees) electrical angle
= “Index Pulse”
“AngleMechanicalNormalized” = normalized (0-1 = 0-360 degrees) mechanical angle

## Slide 7: Encoder – TI Peripheral Block & Results
The eQEP Properties are presented below:
Manually turning the PMSM motor shaft produces the following time history results
View Source Model in VisSim
View Debug Model in VisSim

## Slide 8
Thank You
  For more information please visit;
  http://www.altairhyperworks.com
  Search for VisSim under the Products category