## Slide 2: Corial 200S
Easy-to-use Reactive Ion Etching equipment
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Wide process range for Si, silicon-based compounds, metals and Polymers
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Rapid substrate loading and unloading
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Smaller wafer pieces up to full 200 mm wafer
1x2’’ to 7x2’’ ; 1x3’’ to 3x3’’ ; 1x4’’ ; 1x6’’ ; 1x8’’

## Slide 3: System description Corial 200S

## Slide 4: System description
627
750
357
1080
600
193
420
490
SMALL FOOTPRINT
0.81 m2
Low CoO
General View

## Slide 5: System description
Detailed View
Pumping system
(TMP 500l/s and dry pump 28m3/h)
Chiller / Heater
RIE reactor
HV and LV power supplies
Process controller
300 W RF generator
(13,56 Mhz)

## Slide 6: System description
Loading
Direct loading
FAST LOAD AND UNLOAD
< 210 s
LOADING TIME
Shuttle
EASY EXCHANGE BETWEEN SUBSTRATE SHAPE AND SIZE

## Slide 7: Standard rie source corial 200S

## Slide 8: Rie source
Easy-to-use
Excellent process control enabled by efficient substrate cooling
Retractable liner for sputter-etch increase time between cleans and reduce clean time
shuttle (carrier) design, combined with a standard cathode, for a cost-effective and fast reactor adaptation, suitable for multiple applications and substrate types
Minimized maintenance
For fluorine-based etch processes
SiO2 50 nm/min
Si3N4 60 nm/min
Nb 100 nm/min
…

## Slide 9: Rie source
Operation Sequence
TMP
Laser window
Coolant IN
Coolant OUT
200 mm wafer
A He pressure at 5 Torrs maintains the substrate holder at constant temperature
Helium IN
Substrate
holder
PLASMA
Cathode

## Slide 10: Performances rie processes corial 200S

## Slide 11: Rie of si, oxides, nitrides
Fluorinated chemistry
RIE of SiO2 with PR mask – Vertical profile – High etch uniformity
RIE of SiO2 with PR mask – 0.8 µm deep
RIE of Si3N4 - 0.8 µm deep
RIE of Si – 0.8 µm deep - Anisotropic profile

## Slide 12: Rie of metals
Nb Etching with PR mask – Anisotropic profile
RIE of Nb / Ta
Ti Etching with PR mask - Anisotropic profile
TaEtching with PR mask – Anisotropic profile
Fluorinated chemistry

## Slide 13: High etch rates
Excellent Uniformities
Process | Mask | Etch rate (nm/min) | Selectivity (vs mask) | Uniformity (across wafer)
Polymers | PR | 400 | 1 | ±5%
SiO2 | PR | 50 | 3 | ±3%
Si3N4 | PR | 60 | > 2 | ±3%
Si | PR | 100 | 1 | ±5%
Nb | PR | 100 | > 0.5 | ±5%
Ta | PR | 90 | > 0.5 | ±5%
Ti | PR | 25 | 0.3 | ±5%

## Slide 14: Rie source for sputter-etch Corial 200S

## Slide 15: Sputter-etch
RIE Process Chamber for Etching and Sputtering
LINER TO COLLECT ETCH-BY-PRODUCTS AND SPUTTERED MATERIALS
1 min
Reactor Venting
4 min
Pumping down to 10-4 Tor
5 min
Liner replacement
5 min
Plasma cleaning
EASY LINER replacement by a single person
Dedicated process chamber for
Au, Ag, Ni, Fe, Co, Pt, PZT… SPUTTERING

## Slide 16: Sputter etch
Ar chemistry
Back sputtering of Pt with PR mask
Process | Mask | Etch rate (nm/min) | Selectivity (vs mask) | Uniformity (across wafer)
Au, Pt, PZT, Fe, Co | PR | 45 | > 1 | ±5%

## Slide 17: Shuttle holding approach corial 200S

## Slide 18: Shuttle holding approach
Portfolio
50 mm wafer
75 mm wafer
100 mm wafer
150 mm wafer
200 mm wafer
50 mm wafer
75 mm wafer
100 mm wafer
150 mm wafer
200 mm wafer
NQ200 wafer carrier
NG20 wafer carrier

## Slide 19: Shuttle holding approach
Impact on Performances
Conductive Shuttle
Conductive Shuttle
Thick Quartz
Conductive Shuttle
Optimized Quartz
Positive slope
Negative slope
Vertical slope
SiO2 etching with aSi-H mask

## Slide 20: Shuttle holding approach
Benefits
Quick adaptation to sample shape and size
Optimum process conditions with NO modification of process chamber
Limited cross contamination between processes by using dedicated shuttles
2’’
Wafer carrier

## Slide 21: usability corial 200S

## Slide 22: Process control software
COSMA
The simplest, most efficient software to develop processes, operate, and maintain CORIAL systems
DESKTOP APPLICATION
Process Editing I Process Adjustment I Process Operation I Process Tracability I System Maintenance
REMOTE CONTROL
COSMA
CORIAL OPERATING SYSTEM FOR MACHINE

## Slide 23: Reprocessing software
COSMA RS
REMOTE
ANALYSIS OF RUNS
DISPLAY UP TO 4
PARAMETERS FROM A RUN
DRAG AND DROP
CURVES TO CHECK PROCESS REPEATABILITY
Simple and efficient software to analyze process runs and accelerate process development

## Slide 24: End point detection
EPD with laser
A CCD camera and laser diode, in the same measuring head, enables simultaneous visualization of the wafer surface and the laser beam impact on it. A 20 µm diameter laser spot facilitates the record of interference signals.
Real-Time etch rate measurement
Real-Time etched depth measurement

## Slide 25: Corial 200S
Easy-to-use Reactive Ion Etching equipment
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Wide process range for Si, silicon-based compounds, metals and Polymers
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Rapid substrate loading and unloading
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Smaller wafer pieces up to full 200 mm wafer
1x2’’ to 7x2’’ ; 1x3’’ to 3x3’’ ; 1x4’’ ; 1x6’’ ; 1x8’’