## Slide 2: Corial 210RL
Anisotropic RIE etching supported by a wide range of processes
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
RIE capabilities over a variety of materials including Silicon compounds, metals, polymers, III-V and II-VI compounds
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Modular design approach supporting tiered upgrades
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Smaller wafer pieces up to full 200 mm wafer
1x2’’ to 7x2’’ ; 1x3’’ to 3x3’’ ; 1x4’’ ; 1x6’’ ; 1x8’’

## Slide 3: System description Corial 210RL

## Slide 4: System description
General View
THE MOST
COMPACT
MACHINE
ON THE MARKET
962
750
357
1570
600
420
388
490
SMALL FOOTPRINT
Low CoO

## Slide 5: System description
Detailed View
Pumping system
(TMP 500l/s and dry pump 110 m3/h)
Chiller / Heater
RIE reactor
HV and LV power supplies
Process controller
300 W RF generator
(13,56 Mhz)
Load lock

## Slide 6: System description
Loading
Vacuum robot
FAST AND REPEATABLE LOAD AND UNLOAD
< 180 s
LOADING TIME
Shuttle
EASY EXCHANGE BETWEEN SUBSTRATE SHAPE AND SIZE

## Slide 7: Standard rie source corial 210RL

## Slide 8: Rie source
Anisotropic RIE Etching
Load lock enables using a combination of fluorinated and chlorinated chemistries in the same tool
Load lock for stable and repeatable process conditions
Uniform temperature control for best repeatability
Retractable liner for sputter etch increase time between cleans and reduce clean time
shuttle (carrier) design, combined with a standard cathode, for a cost-effective and fast reactor adaptation, suitable for multiple applications and substrate types
System can be upgraded from a basic RIE tool to an advanced ICP-RIE system
Flexible solution for RIE
SiO2 50 nm/min
Al 250 nm/min
GaAs 300 nm/min
…

## Slide 9: Rie source
Operation Sequence
Cathode
Shuttle Loading
Loading tool
Shuttle
1

## Slide 10: Rie source
Operation Sequence
Loading tool
Cathode
Cathode Up
Shuttle
2

## Slide 11: Rie source
Operation Sequence
Plasma heats wafer and cathode
Cathode
Loading tool
Helium
PLASMA
Coolant IN
Coolant OUT
Heat is transferred to shuttle and to the cooled cathode by He pressure at 5 Torrs
Shuttle
3

## Slide 12: Performances rie processes corial 210RL

## Slide 13: RIE OF Si, OXIDES AND NITRIDES
RIE of SiO2 with PR mask – Vertical profile – High etch uniformity
RIE of SiO2 with PR mask – 0.8 µm deep
RIE of Si3N4 - 0.8 µm deep
RIE of Si – 0.8 µm deep - Anisotropic profile
Fluorinated chemistry

## Slide 14: Rie of metals
Nb etching with PR mask – Anisotropic profile
RIE of Nb / Ta
Ti etching with PR mask - Anisotropic profile
Ta etching with PR mask – Anisotropic profile
Fluorinated chemistry

## Slide 15: Rie of metals
AlCu Etching with PR mask – Selective process
Chlorinated chemistry
Mo Etching with PR mask

## Slide 16: Rie of III-V compounds
RIE of GaAs – High etch rate – High selectivity
RIE of AlGaInP – PR mask
RIE of GaN – SiO2 mask
RIE of InP – High etch rate

## Slide 17: High etch rates
Excellent Uniformities
Process | Mask | Etch rate (nm/min) | Selectivity (vs mask) | Uniformity (across wafer)
Polymers | PR | 400 | 1 | ±5%
SiO2 | PR | 45 | > 2 | ±3%
Si3N4 | PR | 60 | > 2 | ±3%
InP | SiO2 | 80 | > 50 | ±3%
GaN | SiO2 | 200 | 5 | ±5%
GaAs | PR | 300 | 6 | ±5%
Al | PR | 180 | 1 | ±5%
Ta | PR | 90 | > 0.5 | ±5%
Ti | PR | 25 | 0.3 | ±5%
Nb | PR | 110 | > 0.5 | ±5%

## Slide 18: Rie source for sputter-etch Corial 210RL

## Slide 19: Sputter etch
RIE process chamber for etching and sputtering
LINER TO COLLECT ETCH-BY-PRODUCTS AND SPUTTERED MATERIALS
1 min
Reactor Venting
4 min
Pumping down to 10-4 Tor
5 min
Liner replacement
5 min
Plasma cleaning
EASY LINER replacement by a single person
Dedicated process chamber for
Au, Ag, Ni, Fe, Co, Pt, PZT… SPUTTERING

## Slide 20: Sputter etch
Ar chemistry
Back sputtering of Pt with PR mask
Process | Mask | Etch rate (nm/min) | Selectivity (vs mask) | Uniformity (across wafer)
Au, Pt, PZT, Fe, Co | PR | 45 | > 1 | ±5%

## Slide 21: Shuttle holding approach corial 210RL

## Slide 22: Shuttle holding approach
Portfolio
50 mm wafer
75 mm wafer
100 mm wafer
150 mm wafer
200 mm wafer
50 mm wafer
75 mm wafer
100 mm wafer
150 mm wafer
200 mm wafer
NQ200 wafer carrier
NG20 wafer carrier

## Slide 23: Shuttle holding approach
Impact on Performances
Conductive Shuttle
Conductive Shuttle
Thick Quartz
Conductive Shuttle
Optimized Quartz
Positive slope
Negative slope
Vertical slope
SiO2 etching with aSi-H mask

## Slide 24: Shuttle holding approach
Benefits
Quick adaptation to sample shape and size
Optimum process conditions with NO modification of process chamber
Limited cross contamination between processes by using dedicated shuttles
2’’
Wafer carrier

## Slide 25: usability corial 210RL

## Slide 26: Process control software
COSMA
The simplest, most efficient software to develop processes, operate, and maintain CORIAL systems
DESKTOP APPLICATION
Process Editing I Process Adjustment I Process Operation I Process Tracability I System Maintenance
REMOTE CONTROL
COSMA
CORIAL OPERATING SYSTEM FOR MACHINE

## Slide 27: Reprocessing software
COSMA RS
REMOTE
ANALYSIS OF RUNS
DISPLAY UP TO 4
PARAMETERS FROM A RUN
DRAG AND DROP
CURVES TO CHECK PROCESS REPEATABILITY
Simple and efficient software to analyze process runs and accelerate process development

## Slide 28: End point detection
EPD with laser
A CCD camera and laser diode, in the same measuring head, enables simultaneous visualization of the wafer surface and the laser beam impact on it. A 20 µm diameter laser spot facilitates the record of interference signals.
Real-Time etch rate measurement
Real-Time etched depth measurement

## Slide 29: Corial 210RL
Anisotropic RIE etching supported by a wide range of processes
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
RIE capabilities over a variety of materials including Silicon compounds, metals, polymers, III-V and II-VI compounds
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Modular design approach supporting tiered upgrades
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 8.2 | 3.2
Smaller wafer pieces up to full 200 mm wafer
1x2’’ to 7x2’’ ; 1x3’’ to 3x3’’ ; 1x4’’ ; 1x6’’ ; 1x8’’